## Slide 1: Effects of Pedestrians on Traffic Flow of Cars in a 1 Lane, 4 Way Modern Roundabout
Andrew Tucker

## Slide 2: Modern Roundabout
  Classification of a Modern Roundabout vs Nonconforming Traffic Circle from Ourston
Entering traffic yields to traffic already within the circle.
Traffic approaches radially and is deflected around the edge to slow down entering vehicles.
Pedestrians cross the junction at a car’s length away
  A car waiting to enter the roundabout is ahead of where the pedestrian crosses
  A car that just exited the roundabout has a space to wait for a pedestrian to cross
In between lanes, there is an island where pedestrians can safely stand

## Slide 3: Cars
  Original Kinematic Wave model by Lighthill and Windham
  Nagel-Schreckenberg is an example of a Microscopic Traffic Flow model
    These models are primarily concerned with flow and bottlenecking on a highway rather than a junction
Each car behaves as a separate entity (Microscopic Traffic Flow)
  Each car’s behavior is based on decision theory and processed at each tic
Traffic Density: on average, how many cars pass a certain reference point in space per unit of time
  Reference Points:
    Just before a crosswalk on entry at each lane
    Just before a crosswalk on exit at each lane
  Unit of time
    Measured discretely, using “tics,” where a tic is the amount of time it takes a car to travel 1/8th of the interior of the circle, or approximately 0.375s

## Slide 4: Pedestrian
Microscopic Traffic Flow
  Using decision theory to process each pedestrian’s action at each tic
We are not measuring pedestrian density, but the actions of a pedestrian will influence cars trying to enter/exit

## Slide 5: Assumptions Made
Uniformity of Cars, Pedestrians
  Differences in car performance are not significant enough for acceleration/speed to be a factor
    Speed limit within a roundabout is 15-20 mph, which cars can reach and reach quickly
  Drivers are all similarly competent, and will not drive recklessly
    Roundabouts have been demonstrated to have significantly lower accident rates compared to other intersection types (Nambisan)
  Pedestrians are all similarly competent, and will not walk in the way of approaching vehicles
    Roundabouts also reduce the directions a pedestrian needs to watch for cars, from 4 to 1, 1

## Slide 6: Assumptions, cont’d
There will be up to 8 cars in the roundabout at once
Up to 5 pedestrians will attempt to cross a singular crosswalk in a direction at once
  More can be in the process of crossing at any given time, this is for groups starting to cross in a single tic

## Slide 7: Decision Trees
Car
This one is too big to be legible on the slides.
Pedestrian
At center island
Car at exit and moving
Car at entrance and moving
wait
exit
wait
enter
Left -> Yes
Right -> No

## Slide 8: Simulation
Generate a list of cars and pedestrians
  This will always generate the same 150 cars, where a car starts with a location and destination
Until all the cars have made it through the roundabout:
  Evaluate the decision of each pedestrian first
  Evaluate the decision of cars waiting to exit the system
  Evaluate the decision of cars within the traffic circle
  Evaluate the decision of cars that have yet to enter the circle

## Slide 9: Analysis
Unfortunately, the simulation is flawed, and currently the effects of pedestrians are either: nonexistent for sufficiently small numbers of pedestrians, or infinite for sufficiently large numbers
We will use a linear regression model to create a line between the number of pedestrians and the traffic flow, both entering and exiting the roundabout
  The x-axis will be representative of the number of pedestrians
    x=0 corresponds to no pedestrians
  The y-axis will be representative of the average traffic flow across all 4 directions
    We will have 2 graphs, one for entering traffic and one for exiting traffic

## Slide 10: Usefulness of Model
Currently, none. The simulation is not functioning properly.
Will need to evaluate errors of linear regression model to determine accuracy of description of relationship between traffic flow and pedestrian count as linear

## Slide 11: Flaws of Model
Entirely deterministic
  Does not account for human variance
  The simulation operates on the same list of cars, and the first n pedestrians generated will be the same no matter how many pedestrians are generated
Pedestrians have right-of-way
  Cannot add all the pedestrians at once and have them flow through the system in the same way.
  This means that whether or not a pedestrian effects the system, and to what extent, is determinant on the current traffic flow
    If a pedestrian would be added after all the cars have passed through, then the pedestrian would not influence the flow
    Once all the pedestrians have gone through the traffic circle, then the rest of the model plays out as if there were no pedestrians, influencing traffic flow